from Czaroom [4.13] …Brake parts
I'll restate my comments for any new owner.
I ordered and installed two front brake wheel cylinders from a Ford Think (NEV) $22.00+ship. They bolted on with no modifications and work fine.
I also installed a Ford Think Master Cylinder several Months ago and that also worked out fine (no modifications) $68.00+ship.
Both are available from the below site:

http://www.nevaccessories.com/FORD-T...info/THK-WC-F/

http://www.nevaccessories.com/Ford-T...fo/THK-MASCYL/

___________________________________________________________________

“THE DOWNEAST UPDATE"………………………..

Access to aux battery, the correct cut out size is 5" by 9", must be careful of wires in the tunnel.

I think the 2000 year models had these battery access doors under the seats[3.13]

2000					???? home made ????

--------------------------------------------------------------------------------------

“Czaroom master cylinder replacement”………….[3.13]

Master Cylinder from a Ford Think is a Direct replacement...

Peacock wanted $393.00 but I bought one on e-Bay for $99.00.

Also available at nevaccessories.com

There is a e-bay listing for $68 + shipping...

They use a remote Brake Fluid Reservoir, so you will need to use your old Tank.

The rest was pretty much a bolt-on.
--------------------------------------------------------------------------------------

I just ordered two Think Wheel Cylinders... I'll repost if they fit.

----------------------------------------------------------------------

“THE FLASH UPDATE”…………………. master cylinder replacement

My brake master cylinder went bad. Peacock wants $200 for a new Bombardier master cylinder. After spending 45 minutes at Napa auto parts going through a book of few hundred master cylinder (most of which are no longer available) I found one that had the correct 3/4 inch piston size and is about the right size and shape. It's from a 1954 - 1962 VW beetle.$27.99. It's close to a perfect fit. The mounting holes are just a little too wide. I enlongated the holes on the bomber mounting bracket with a die grinder. A rat tail file would do it also if you don't have a die grinder. Next you have a choice of enlarging the mounting bracket hole or using a couple of larger nuts as spacers so the mounting ears on the master cylinder won't snap off as you tightnen the mounting bolts.
Next, the Bombardier pushrod is too short for the VW master cylinder. I cut the rod off of the pushrod clevis, drilled a 5/16 hole in the clevis and welded on a nut onto the clevis so I could use a threaded bolt as a pushrod. This allows for an adjustable pedal height. If you don't have a welder you could grind down a nut to fit inside the clevis so you can use this nut on the inside of the clevis and a second nut on the outside to bolt the pushrod bolt onto the clevis securely. Cut of the bolt head, round out the end of the bolt where you cut the head off adn you have a custom adjustable pushrod ready to install.
Parts list:
1. Master cylinder- Napa part number M35125 $27.95
2. Bleeder screw - Napa part number UP 22069 $2.39
3. Plug for end of master cylinder $1.59
4. 3/16 to 10mm brass brqke line adapter- Dorman 071340 $6.50

Total cost $38.43 instead of $200 plus shipping and it works perfectly.

Pic 1. The stock cyl on top. VW cyl on bottom. Notice plugs in extra holes. Cyl came with one. Bleeder screw helpful in extracting air from system as well as plugging hole.
pic 2. Stock clevis.
pic 3. Modified clevis before cutting the head of bolt off. old unused brake line adapter from stock cyl. wrong threads.
pic 4. Installed VW cyl. (notice nuts used as spacers between mounting ears and mounting bracket and 3/16 to 10MM brake line adapter)
Pic 5. Installed and funtioning pushrod.

----------------------------------------------------------------------

“FLASH WHEEL CYLINDER UPDATE”…………………..

If you ever need a brake wheel cylinder I found one that you can buy new for $13. From the new one, you can remove the pistons with both seals and put them in your cylinder. It works great. I bought it at Auto Zone. The brand name is Brakeware and the part number is 30173.
On the package it says it is a replacement for:
Wagner F131262
Raybestos WC37997
Bendix 34112

The pistons are a little longer and space the brakes shoes just wide enough to be a problem with fitting the brake drum. cut slots in the end of the pistons where the brake shoe rests against the piston that will match the slots in the stock pistons so you will have clearance for the shoes to brake drum.

SEE Czaroom comment on think replacement above[3.13]

----------------------------------------------------------------------

“HINTS”……………………

Replace the black Velcro strips, used for the cloth doors, [if you have them] on body with white ones, looks a lot better..

[2.13]

Question…The other more painful issue is the cart stops randomly. You can try to put it into drive but it doesn't even show up on the dash. It will show R for reverse at that point when you turn the key but won't go in reverse either. May be two separate issues? Just waiting and messing with the key seems to get it going again (randomly)…

Answer…."It will show R" ???? my bom has several micro lever switches....make sure they are not loose and make sure the key sw lines up with the decal on the dash….

"cart stops randomly" check to make sure the break pedal is returning all the way.

Result….The issue with it just stopping was fixed so far with a good cleaning of the ignition contacts with CRC spray lubricant and compressed air. It was not making good contact in the "D" position and "N".

Comment….good observation and fix....although these micro switches are "semi sealed" and this is a clean area, I would not have considered this., but in my last life I have seen this type of switch completely packed with fine dust/dirt. [I am assuming your model has the micro stacked key assembly]

“NEVerland comment” cluster accuracy…………….

The cluster is WAY inaccurate. Showed almost full discharge after 10.4 miles and the programmer shows 70 volts left in the pack. Going to full charge and reset the cluster to see if that gets the cluster accurate.

“EWPWBWI”

My bom indicates the same 10.4m/70v

“Downeast10”

It should reset the charge gauge by removing the cluster and unplugging from the back, then plug back in

“BATTERY GAGE RESET”

I unpluged the cluster and reconnect, did this and you can see from my log [email] there was a change, but no opinion on my part as to why, how or what. just have not run it enuf after repluging. It seems that 9-10 miles puts batt at 90% [newer batteries] and "gas gage" at 3 [1 being at the left or low, 8 being full] there was someone else that indicated 10 miles and gage at 3.

_________________________________________________________________